| Event / Facility Date | Repton Parish Council speed Indicator Devices |
| --- | --- |
| Organizer / Point of Contact | Repton Parish Council |
| Site | Milton Road, Milton, inbound to Milton Milton Road, outbound lamppost number 66564 Milton Road, outbound lamppost number 60568 Milton Road, inbound, opposite lamppost number 91085 High Street, inbound Back of “Humps” warning sign Burton Road outbound lamppost number 6646366463 |
| Event Insurance | Repton Parish Council insurers |
| Type of Event | Installing, moving, rotating or working on Speed Indicator Device |
| Audience | Parish Councillors |
| Previous Experience | N/A |
| Walk down by (check before event) | Before any work is commenced on SIDs |
| Comments |  |

| What are the hazards? | Who might be harmed and how? | What are you already doing? | Do you need to do anything else to control this risk? | Action by whom? | Action by when? | Done |
| --- | --- | --- | --- | --- | --- | --- |
| Vehicle parking adjacent the deployment site during installation. Risk of obstruction. | Injury to operatives and other road and footpath users whilst work being carried out | Councillors performing activity should Ask owner to move vehicle if possible | No | N/A | N/A | N/A |
| Traffic including motorcycles will be travelling in both directions and potentially at speed. There is a potential for drivers to carry out inappropriate procedures. | Injury to operatives and other road and footpath users whilst work being carried out | Councillors performing activity should: Wear High-vis tabbards Allocate someone to monitor traffic Move when vehicles approach Carry out work between 10am and 2pm to avoid peak traffic Check for and remove any debris in road | No | N/A | N/A | N/A |
| Pedestrians using the pathways during work, risk of injury | Injury to operatives and other road and footpath users whilst work being carried out | Councillors performing activity should: Allocate someone to be a look-out Tape off area with barrier tape while working Wear high vis Stop work until pedestrians have vacated immediate vicinity. | No | N/A | N/A | N/A |
| SID becomes unattached from the pole | Injury to operatives and other road and footpath users whilst work being carried out | Parish Council Public Liability Insurance | No | N/A | N/A | N/A |
| Handling hazards | Injury to operatives and other road and footpath users whilst work being carried out | Councillors performing activity should: When working on the SID a free standing stepladder with outriggers at its base should be used to accommodate soft ground. The stepladder is not to be positioned on the "live highway" side of the pole. When removing the SID from its location or rotating SID, batteries should be removed in the first instance and then the SID removed from its mount. | No | N/A | N/A | N/A |
| Rotation or moving of the SID | Injury to operatives and other road and footpath users whilst work being carried out | Minimum of three people required to undertake activity, one of whom should be monitoring road and/or footpath traffic Wear High-vis tabbards. | No | N/A | N/A | N/A |

Risk Assessment Prepared by: Caroline Crowder Clerk to Repton Parish Council

Date Approved by Repton Parish Council: March 2024

Reviewed/Updated: N/A

Next Review Due: March 2025

# Text boxes

# Repton Parish Council Risk Assessment